## Slide 1
探测器--
用于数据中心网络的拓扑感知监视系统
组员：
石建良
丁轩昂
张志强
演讲者：石建良
（deTector: a Topology-Aware Monitoring System for Data Center Networks）
第六组

## Slide 2: 目 录
1.背景与现状
2.目前挑战
3.现存方案
4.改进方案

## Slide 3
1
1.至少有8个主机的网络需要维护
2.至少有15个路由器发生了故障或重新加载了
3.至少有26个机架坏了 or 需要迁移
4. Dozens of blips of DNS（几十个DNS需要做标记？）
5. 至少有1000台个体机发生了故障
Typical first year for a new cluster
      SLA violation (99.999%)
1.包的丢失和峰值的延迟
2.很难去寻找故障源并解决这个问题需要几天的时间
1.背景与现状
SLA violation（99.999%）
2
数
据
中
心
的
网
络
监
控
Failures are the norm rather than exception

## Slide 4
1
1.至少有8个主机的网络网络需要维护
2.至少有15个路由器发生了故障或重新加载了
3.至少有26个机架坏了 or 需要迁移
4. Dozens of blips of DNS（几十个DNS需要做标记？）
5. 至少有1000台个体机发生了故障
Typical first year for a new cluster
      SLA violation (99.999%)
1.包的丢失和峰值的延迟
2.很难去寻找故障源并解决这个问题需要几天的时间
1.背景与现状
SLA violation（99.999%）
2
数
据
中
心
的
网
络
监
控
Failures are the norm rather than exception
而对于一个数据中心的网络监控系统需要迅速的故障恢复机制，否则造成的后果无法度量

## Slide 5
2.目前挑战
Clean failures
Gray failures
Low-rate losses
Transient failures
比如说：故障清理的力度，能否完全清理完？
一些设备无法报告故障
由等价路由造成的路由器路径被覆盖的问题
很难精准的捕捉、定位、回滚

## Slide 6
2.目前挑战
1.故障的清理
2.灰色地带的故障
3.降低损失率
4.转瞬及时的故障
比如说：故障清理的力度，能否完全清理完？
一些设备无法报告故障
由等价路由造成的路由器路径被覆盖的问题
很难精准的捕捉、定位、回滚
面对这些挑战，因此我们需要尽可能的详尽的检测

## Slide 7
3.现存方案
Existing systems
  Passive: CLI/SNMP
  Active: Pingmesh, NetNORAD
Limitations
  Fail to detect at least one type of losses
  High overhead
– Can not pinpoint failures without other tools (e.g., tracert)

## Slide 8
3.现存方案
Existing systems
  Passive: CLI/SNMP
  Active: Pingmesh, NetNORAD
Limitations
  Fail to detect at least one type of losses
  High overhead
– Can not pinpoint failures without other tools (e.g., tracert)
因此我们需要进行改进：
我们可以利用网络的拓扑结构去设计一个更好的网络检测系统

## Slide 9
4.改进方案
Phase I: Path Computation
Phase II: Network Probing
Phase III: Loss Localization
探
测
器

## Slide 10: deTector in One Slide
Controller
Diagnoser
1. Path computation
2. Network probing
3. Loss localization
Pinger
Pinglist
Responder
Logs
UDP Probes
探索
5

## Slide 11
Phase I: Path Computation

## Slide 12: Path Selection Problem
1 | 1 | 0
1 | 0 | 1
0 | 0 | 1
Path 1
Path 2
Path 3
Link 1
Link 2
Link 3
Given a routing matrix, select probing paths to send probes:
  最小化路径数
  α-覆盖
  β-识别能力

## Slide 13: α-覆盖
Ensure even and enough path coverage of each link
我们应用链路权重w[link]，来表示链路所在的路径数.
If w[link] > α, 则链接有足够的路径去覆盖它.
1 | 1 | 0
1 | 0 | 1
0 | 0 | 1
Path 1
Path 2
Path 3
Link 1
Link 2
Link 3
每个链路被探测矩阵中的至少α个路径覆盖

## Slide 14: β-识别
再DCN中任何个β链路的同时故障可以被正确识别
探测矩阵: path1 + path2
1-identifiability but not 2- identifiability
1,2
1
2
1 | 1 | 0
1 | 0 | 1
0 | 0 | 1
Path 1
Path 2
Path 3
Link 1
Link 2
Link 3

## Slide 15: 从1-识别到β识别的扩展
1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
Link 12
Link 13
Link 23
含有虚拟链路的扩展路由矩阵
如果一个虚拟链路发生down机了，则它相对应的物理链路发生了故障.
OR
Physical links
Virtual links
Path 1
Path 2
Path 3
Link 1
Link 2
Link 3

## Slide 16: 1-识别算法
L
选择一个路径
Greedily select the path which splits the largest number of link sets in each iteration
L
L1
L2
L11
L12
L21
L22
L111
L112
L121
L122
L211
L212
L221
L222
选择一个路径
选择一个路径

## Slide 17: Probe Matrix Construction (PMC) Algorithm
对每条路径定义一个分数
扩展矩阵含有虚拟链路
Quantify
coverage
Quantify identifiability
再每次迭代中，总是选择最低分的路径
当探测矩阵实现α覆盖和β识别,则循环停止

## Slide 18
PMC算法过程

## Slide 19
PMC算法过程
1.到达了63%的近似率
2. Fattree（64）DCN具有超过232条路径，运行时间> 24小时

## Slide 20
1 1 0 | 0 0 |  | 
1 0 1 | 0 0 |  | 
0 1 1 | 0 0 |  | 
0 0 0 |  | 1 0 | 
0 0 0 |  | 1 1 | 
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
1
0
1
1
PMC算法的加速（改进）
优化 I: Routing Matrix Decomposition

## Slide 21
尽可能延长路径的分数更新，直到我们必须.
该启发式的正确性通过路径集的分数的子模态来保证.
Score heap
仅只更新位于堆顶的路径分数
path 1
path 3
path 2
path 5
path 4
优化 II: Lazy Update

## Slide 22
优化 III: Symmetry Reduction
•
Most DCN topologies are symmetric!

## Slide 23: Fattree的PMC算法结果
Running time on one Xeon E5-2620 CPU
From days to
17
seconds

## Slide 24: Fattree的PMC算法结果
Running time on one Xeon E5-2620 CPU
The number of probe paths
The optimal needs at least 52428 paths
From days to
17
seconds

## Slide 25
Phase II: Network Probing

## Slide 26: Network Probing
UDP probes: varying packet length, DSCP, source port
Source routing: IP-in-IP encapsulation and decapsulation
Responders: simply echo probes back

## Slide 27
Phase III: Loss Localization

## Slide 28: Loss Localization Problem
1 | 1 | 0
1 | 0 | 1
0 | 0 | 1
Path 1
Path 2
Path 3
Link 1
Link 2
Link 3
Given the probe matrix and loss measurements, select the least number of links
to explain the observation.
NP-hard
Loss
measurements
4
1
3

## Slide 29: Packet Loss Localization (PLL) Algorithm
In each iteration we select a link that can explain the largest number of probe losses until all are explained
  If a link lies in the packet path, then the link can explain the loss.
Two simple improvements
  Matrix decomposition to speedup computation
  Use threshold to filter false positives
    The ratio of # of lossy paths over # of all probe paths through the link

## Slide 30: 分析
在18-radix Fattree中的准确度，具有不同水平的α覆盖和β可识别性的探针矩阵
26

## Slide 31: Summary
The core of deTector is a carefully designed probe matrix, enabling fast and accurate loss detection and localization.
deTector is practically deployable.

## Slide 32
Discussion
Packet entropy
Loss diagnosis
- Beyond deTector

## Slide 33
Thank